## Slide 1: Coastal Zones: Processes and Landforms

## Slide 2: Definitions of Coastal Regions:
The shore is the area on the coast which covers the furthest low tide mark to the highest elevation where waves affect (width: a few to hundreds of meters)
The coast extends from the inland edge of the shore as far inland as ocean-related features are found. (width: less than a km to many tens of kms)
  The coastline marks the boundary between the ocean and the land

## Slide 4: Backshore and Foreshore
The backshore refers to the part of the coast that is above the high tide line
The foreshore refers to the part of the coast that is covered at high tide; exposed at low tide
  The foreshore also can be called the intertidal zone

## Slide 6: Backshore and Foreshore
The nearshore refers to the area between the shoreline (water’s edge) and the zone where waves are breaking.
Offshore refers to the area where water is too deep to affect waves.
Offshore Oil Drilling

## Slide 7: Coastline (vs) Shoreline
Read over the statistics of coastline and shorelines for each province and territory in Canada.
Answer the questions.

## Slide 8: The Beach
The beach is the part of the coastline which has sediment deposited (i.e. sand)
  The berm is the dry part of the beach, above the high tide mark
Off the shoreline is the longshore bar (known commonly as the sand bar) is formed at certain points of the year
  It is exposed to the air during low tides

## Slide 9: Composition of the Beach
Beaches are composed by material that is available in that geographical location
  For example, in Joggins, Nova Scotia the cliffs surrounding the beach are made of thin, brittle rocks (known as shale) which form the beach.
  If there is a lot of fine material in a region the beaches can be made of mud or sand; if there are volcanoes then the beach is made of weathered volcanic rocks (basalt)

## Slide 10: Movement of Sand
Sand can move both up and down the beach as well as side to side (longitudinally)
  Sand moves up and down the beach due to breaking waves
    A wave swashes (breaks and moves in) and then backwashes (draws back)

## Slide 11: Movement of Sand (Cont’d)
Longitudinal motion of sand takes place because of an along shore current
  Waves bend as they approach the shore (rarely they hit the shore straight on)
  This creates a zig zag pattern

## Slide 12: Features of an Erosion Coast
Any land that sticks out from the coast will bear the brunt of the energy from breaking waves. We call these areas headlands
Wave action can create sea cliffs or even sea caves from the repeated swashing motion
Some waves can wear a tunnel through part of the sea cliff and form a sea arch
  This ultimately can wear away forming a sea stack, which is a high tower of sea cliff

## Slide 14: Features of Depositional Shores
A shore that can build up its sediment (sand) is said to be a depositional shore

## Slide 15: Features of Depositional Shores
A spit is a linear ridge that sticks out in the direction of the longshore current; the end of the spit will curve into the bay as it gets bent inward by currents
A bay barrier is a barrier that separates a bay from the open ocean. These form when the currents are not strong enough to keep the mouth of the bay open
A tombolo is a ridge of land which connects an island or sea stack to the mainland

## Slide 16: Features of a Depositional Shores
Longshore current: currents of water flowing parallel to the shore. They are formed by waves striking the shore at an angle. Carry sand and other sediments.

## Slide 17: Risks to Our Coasts
Our shores are at risk due to various human activities which can directly and indirectly affect erosion processes (That is, processes where the coast is worn away)
  Climate change and sea level rise
  Loss of the Berm (loss of sand)
  Interference in the longshore current

## Slide 18: Hard stabilization
Refers to human efforts to build structures that will slow or stop the damage to our coast lines
  It is also called coast armoring of the shore
It can lead to many predictable, yet unwanted, effects

## Slide 19: Groins
Groins are built perpendicular to the shoreline and are designed to trap sand and stop longshore drift (the movement of sand down the beach by the zig-zag motion)

## Slide 21: Jetties
A jetty is similar to a groin as it is designed to protect the shore from unwanted erosion.
They are built to protect the entrance to harbours.

## Slide 23: Breakwater
These will help disperse some of the energy of waves which will slow erosion and increase deposition along it
  This protects areas which you may not want increased deposition (harbour entrance)

## Slide 24: Oak Island Marina

## Slide 25: Sea Wall
Sea walls are built parallel to the shore and are designed to protect beach front properties from the relentless action of ocean waves

## Slide 26: Alternatives to Hard Stabilizations
Hard stabilizations have many drawbacks so there are three major alternatives:
  Beach replenishment – replace sand that is lost due to erosion
  Construction Restrictions – do not allow construction in high risk areas.
  Relocation – Relocate properties at risk

## Slide 27: Pros and Cons – Hard Stabilizations
http://stateofthecoast.noaa.gov/shoreline/shoreline_armoring.html